## Slide 1: 19AIE113 – INTRODUCTION TO ELECTRONICS
Deepthi Sudharsan (CB.EN.U4AIE19022)
Isha Indhu S ((CB.EN.U4AIE19030)
Jayashree O. (CB.EN.U4AIE19031)
Kavya S Kumar(CB.EN.U4AIE19037)
Lakshaya Karthikeyan (CB.EN.U4AIE19039)

## Slide 2: Aim
To design a differential amplifier using transistors and use the differential circuit to design a voltage comparator circuit
Simulation platforms for obtained circuit:
  MultiSim
  TinkerCad
Hardware implementation using ADALM module and ALICE M1K desktop

## Slide 3: Differential Amplifier
Used to amplify the difference between given inputs
Vout = A(V1-V2)
Implemented using BJTs (Q1 & Q2)
In PNP transistors:
  Emitter-Base junction is forward biased
  Collector-Base junction is reversed biased
V1
V2

## Slide 4: Voltage Comparator using Op-Amps
Inverting input: VREF
Non-inverting input: Vin
When Vin<VREF, Vout = 0
When Vin>VREF, Vout = VCC
Notes: Summarize your research in three to five points.

## Slide 5: Voltage Comparator using differential amplifier
Components:
Two PNP BJTs
One 5V DC power supply
AC power supply (Triangular 5V)
One 220μF capacitor
Connecting wires
Resistors Required:
  Two 20kΩ
  Two 10kΩ
  One 6.8kΩ

## Slide 6: Theory behind the circuit
When V1 < Vref (2.5V): Q1 - Conducts
When V1 > Vref (2.5V): Q2 -Conducts
In a voltage comparator circuit, the expected output is:
  When Vin<VREF, Vout = 0
  When Vin>VREF, Vout = VCC
Hence, voltage is measured at Q2’s collector

## Slide 7: Output using Multisim
Purple (PR3) = Reference Voltage
Orange (PR4) = Input Triangular wave
Green (PR1) = Output

## Slide 8: TINKERCAD Implementation
Input
Output
Vref

## Slide 9: ADALM Implementation

## Slide 10: Output using ADALM

## Slide 11: Observation Table
CHANNEL A VOLTAGE | CHANNEL B VOLTAGE
3.0V | 2.6861V
2.7V | 2.6842V
2.3V | 0.0078V
1V | 0.0061V
Reference voltage (chosen) = 2.5V

## Slide 12: Inference
For any input AC waveform:
  Case 1: Vin exceeds 2.5V at any point
    The output will always be a square wave
    In figure, positive half cycle of sine wave
  Case 2: Vin does not exceed 2.5V
    The output will be a straight line of 0V
    In figure, negative half cycle of sine wave

## Slide 13: Limitations of Transistor Circuit
Theoretically, the peak amplitude of the output square wave should be equal to Vcc (V2)
However, due to the voltage drop across the transistors and resistors, the output voltage obtained is less than the expected output voltage
This can be combatted by using MOS transistors.

## Slide 14: References
https://www.electrical4u.com/differential-amplifier/
https://www.electronics-tutorials.ws/opamp/opamp_1.html?utm_referrer=https%3A%2F%2Fwww.google.com%2F
https://youtu.be/ehekdOHOIZ0
http://www.circuitstoday.com/op-amps-operational-amplifiers
http://www.bristolwatch.com/ele/vc.htm